VESSEL CASUALTY No. 15 of 2017

Vessel Destination: EUROPE

“WOTAN” - ENI:04808390 – Flag: Germany – Type: Tanker 
On May 21, the "Wotan" ran aground outside the fairway on the Scheldt-Rhine-Canal. The ship got stuck in a bight at Tholen. The tug "Furie 3" pulled the ship off again. The barge was underway from Antwerp to Rotterdam and berthed in the Neckar Port on May 22.
 
“ZIRCON” - IMO:9010929 – Flag: Latvia – Type: Tanker 
On May 25, a fire broke out in the engine room of the "Zircone" in the Gulf of Riga, Latvia, shortly after leaving the port of Riga, bound for Skaw. The tanker, loaded with 7,000 tons of diesel oil and still adrift was disabled and started to drift, tugs and CG patrol boats were sent to ship. A helicopter with thermal video equipment found high temperature in the superstructure. Two patrol boats "Klints - KA 09", "Skrunda" and the Latvian tug "Stella" (IMO: 9389655) had reached the Zircon.  After the engine room fire was under control the casualty was pulled to the Riga Shipyard - LVRIX - 0035, where she berthed early on May 26.
 
“EEMS DELFIA” - IMO:8411633 – Flag: Netherlands – Type: General Cargo Ship
On May 27, the "Eems Delfia", loaded with construction material, ran aground off the port of Wangerooge. Tugs were able to refloat the vessel which was ordered into the port of Wangerooge for inspections. The water police in Wilhelmshaven launched an investigation. Obviously a combination of currents, wind and fog contributed to the accident. The ship left the port again on May 28 at next being bound to Hausvik, ETA May 30.
 
“HYDRA” - IMO:9356488 – Flag: Netherlands – Type: General Cargo Ship
On May 27, the "Hydra" en route from Nyköping to Antwerp, ran into the embankment of the Kiel Canal at Rüsterbergen during the westbound transit. The ship which had passed the locks in Kiel Holtenau suffered a fire in the switchboard in the engine room and got stuck at the southern shore. The tugs "Bugsier 15" and "Wal" were deployed from Brunsbüttel to pull the ship out. After it was refloated, it berthed at the South Quay of the canal port in Brunsbüttel.

Vessel Destination: AFRICA

“NEW LEGEND - IMO:9230505 – Flag: Liberia – Type: Tanker
On May 23, the crude oil tanker New Legend reportedly ran aground on 62 kilometer mark in Suez Canal, while transiting in southern direction. Four tugs were sent to assist tanker, which was partially blocking traffic. The tanker was refloated and completed transit in the evening same day, after safety check. There were no damages and the "New Legend" left Suez at night May 23 and is under way continuing her voyage from Novorossiysk Russia to Vadinar India

.*********